GENERAL REQUIREMENTS

1    Log book presented.

2    Number & class displayed correctly.

3 Kill switch, lanyard operated.

4 Kill switch operable without removing hands.

5 Fuel shutoff operable from normal riding position (Gas Class)

6 Fuel shutoff operable without removing hands (Fuel Class)

7 Self closing throttle.

8 Fork stops limit travel, not damper.

9 Headlight taped.

10 Mirrors removed.

11 Tires meet speed ratings & good condition.

12 Metal tire valve caps and stems.

13 Axle nuts secured.

14 Steering damper installed (over 125 mph).

15 Brake operation.

16 Chain guard installed.

17 Seat or tail section not over 42”.

18 General inspection for loose parts, tight spokes, welds, etc.

RIDING APPAREL

1 Helmet, full face, Snell 2000 - ECTA sticker

2 Leathers, one piece or metal zippered 270 degrees.

3 Boots,  8” tall leather racing type.

4 Gloves, full leather.

PRODUCTION FRAME

1 Documentation to meet Production Motorcycle class.

2 Foot rests in original location.

3 Original external view, fairings, lights etc.

4 Exhaust, stock appearance, including outlet diameter.

MODIFIED FRAME

1 Wheelbase, 68” maximum.

2 Seat and grips are higher than wheel rims.

3 Rear fender, extend to centerline of rear axle.

4 Foot rests 6” ahead of rear axles.

5 No center hub steering.

6 Non-stock gas tanks, minimum 1.32 gal.

7 Front tire visible from either side for 180 degrees.

8 Rear wheel visible, vertical line, for 180 degrees.

9 One engine, maximum 3000+cc.

SPECIAL CONSTRUCTION

1 A-Frame

2 Foot rest provided.

3 Wheels at least 15”diameter.

4 Center hub steering allowed.

5 Low speed handling & stability demonstrated.

6 Rear fender extend to centerline of rear axle.

7 One or two engines no max size.

PARTIAL STREAMLINING

1 Fairings, 3-point mounts.

2 Streamling covering front wheel.

3 No streamling forward of front rim.

4 Front wheel rim visible 180 degrees.

5 Rear wheel rim visible 180 degrees from axle.

6 Seat or tail extends no more than 3” past rear tire.

7 Rider visible from above and sides.