Buell  chin fairing installation

TO GET YOU STARTED......YOU SHOULD HAVE 5 BOLTS.

2 LONG, 2 SHORT AND 1 EVEN SHORTER THAT IS A BUTTON HEAD. THERE SHOULD

ALSO BE 4 ALUMINUM SPACERS, 4 METAL WASHERS, 4 RUBBER WASHERS, 1 PLASTIC

WASHER, 1 WELL NUT AND A BRACKET. THE 2 LONG BOLTS GET A METAL WASHER THEN A RUBBER WASHER, THE SAME WITH THE 2 SHORTER BOLTS. THE SINGLE BUTTON HEAD GETS THE PLASTIC WASHER. THE BRACKET BOLTS ON TO THE FRONT SHOCK BOLT. YOU WILL NEED TO REMOVE THE FRONT SHOCK BOLT TO INSTALL THE BRACKET. THIS CAN BE TRICKY IF YOU DO NOT HAVE A LIFT OR CENTER STAND.

I HAVE DONE IT SEVERAL TIMES BY HAVING A FRIEND HELP. YOU REMOVE THE NUT AND WASHER FROM THE FRONT SHOCK BOLT. YOU STAND ON THE RIGHT SIDE (CARB SIDE) THE FRIEND STANDS ON THE LEFT.

WITH THE KICKSTAND DOWN, YOU PUSH A LITTLE WHILE THE FRIEND PULLS.....YOU BALANCE THE BIKE ON THE KICK STAND AND THE FRONT TIRE, THE BACK WHEEL WILL BE A "LITTLE" OFF THE GROUND. WHILE YOUR FRIEND HOLDS IT....YOU PULL THE FRONT SHOCK BOLT OUT (THE REAR TIRE MAY DROP.....THAT IS WHY WHEN YOU PULL

IT OVER YOU JUST GET THE BACK TIRE SLIGHTLY OFF THE GROUND) YOU PUT THE

SHOCK BOLT THROUGH THE BRACKET (THE PART THAT IS AT A 90 DEGREE ANGLE)

AND RIGHT BACK THROUGH THE SHOCK MOUNT HOLE AND SHOCK EYE. YOU MAY NEED TO HAVE YOUR FRIEND EASE THE BIKE BACK TOWARDS YOU SO THE SHOCK WILL COME

FORWARD. YOU WILL NEED TO GUIDE THE SHOCK WITH YOUR LEFT HAND WHILE INSTALLING THE BOLT/BRACKET WITH YOUR RIGHT HAND. ONCE THE BOLT IS ALL THE WAY THROUGH THE SHOCK BRACKET AND SHOCK EYE, YOUR FRIEND CAN EASE DOWN THE BIKE. THIS ONLY TAKES A FEW SECONDS FOR THE WHOLE BALANCING ACT.

NOW, THE WAY THE BRACKET NEEDS TO BE POSITIONED WHEN YOU INSTALL THE FRONT SHOCK BOLT. THE 90 DEGREE PART NEEDS TO BE TURNING DOWN, THE LIP NEEDS TO BE TOWARD THE REAR  THEN THE 45 DEGREE PART WILL BE TURNED UP. THAT HOLE IS WHERE THE WELL NUT GOES.

YOU JUST PUSH IT IN WITH THE LIP OF THE WELL NUT TO THE OUTSIDE.  YOU CAN

PUT THE WASHER AND NUT BACK ON THE SHOCK BOLT BUT DO NOT TIGHTEN YET.

REMOVE THE TWO BOLTS AT THE REAR OF THE SWING ARM BRACE (THE ALUMINUM THING OVER THE FRONT PULLEY/SPROCKET THAT SAYS "BUELL") NOW INSTALL INTO THE HOLES THAT YOU JUST REMOVED THE TWO BOLTS FROM THE 2 SMALLER ALUMINUM SPACERS, YOU WILL NEED TO "PUSH" THEM IN.  THIS IS WHERE THE TWO SHORT "FLAT HEAD" BOLTS GO.

THE BOLTS GO IN WITH THE METAL WASHER THEN THE RUBBER WASHER ON THE

BOLT, THE BOLTS GO THROUGH THE THE CHIN FAIRING, THEN THROUGH THE TWO LITTLE STEPPED ALUMINUM SPACERS THAT YOU JUST PUSHED INTO THE SWING ARM BRACE.

ON THE SHIFTER SIDE.....YOU REMOVE THE TWO CENTER BOTTOM BOLTS THAT ARE IN

THE LITTLE "CUT OUT" AREA AT THE BOTTOM CENTER OF THE PRIMARY COVER. THE

TWO LONG BOLTS (WITH THE METAL, THEN RUBBER WASHERS INSTALLED) GOES THROUGH THE FAIRING, THEN THROUGH THE BIGGER AROUND ALUMINUM SPACERS AND INTO THETWO LOWER CENTER PRIMARY BOLT HOLES THAT YOU JUST REMOVED THE TWO BOLTS FROM.

NOW, INSTALL THE SINGLE BUTTON HEAD BOLT WITH PLASTIC WASHER INSTALLED

THROUGH THE CHIN FAIRING INTO THE THE WELL NUT PREVIOUSLY INSTALLED IN

THE SHOCK BRACKET. AFTER ALL BOLTS ARE INSTALLED HAND TIGHT YOU CAN START

"SNUGGING" THEM UP. YOU MAY NEED TO REACH UP UNDER THE FAIRING AND HOLD

THE WELL NUT TO KEEP IT FROM SPINNING UNTIL IT "SWELLS UP" AND GRIPS THE

HOLE. AFTER THE SPOILER IS MOUNTED....YOU CAN TIGHTEN UP THE FRONT SHOCK BOLT

AND

RIDE!